Name ________________________	PHY2048C, Quiz 7

A- Read all the quiz once, or twice, before beginning to write. Make sure to comprehend all questions and start with those you feel most confident in.
B – Be clear and concise. There are no extra points for being verbose or writing extra.
C –Only use the white pages that I will provide. You have 60 minutes to answer the quiz.
---------------------------------------------------------------------------------------------------------------------------
Problem 1
Write down the equation of motion for a mass m hanging from a spring of force constant k. Show that the variable x̃(t) = (x(t) − x0 ), where kx0 = mg, obeys the equation for an oscillator at the same frequency:

(that is, an oscillator that is not under the influence of gravity, just the spring force)

Problem 2

Problem 3

An 1kg mass attached to a vertical relaxed spring descends by 4cm before beginning to move back up in the course of its oscillations. Visualize the oscillation, in particular the end points. (i) What is the amplitude A?