Name ________________________
     PHY2049C, Quiz 6

A- Read all the quiz once, or twice, before beginning to write. Make sure to comprehend all questions and start with those you fell most confident.
B – Be clear and concise. There are no extra points for being verbose or writing extra.
C –Only use the white pages that I will provide. You have 50 minutes to answer the quiz.
---------------------------------------------------------------------------------------------------------------------------
Problem 1 (Wolfson and Passachoff)

Figure 1 shows a simple mass spectrometer, designed to analyze and separate atomic and molecular ions with different charge-to-mass ratios. In the design shown, ions are accelerated through a potential difference V, after which they enter a region containing a uniform magnetic field. They describe semicircular paths in the magnetic field, and land on a detector a lateral distance x from where they entered the field region, as shown. Show that x is given by:

x = 2 over B Sqrt{{2V} over {q/m}}

where B is the magnetic field strength, V the accelerating potential, and q/m the charge-to-mass ratio of the ion. By counting the number of ions accumulated at different positions x, one can determine the relative abundances of different atomic or molecular species in a sample.

    Figure 1
Problem 2

A circular wire loop of mass m and radius R carries a current I. The loop is hanging horizontally below a cylindrical bar magnet, suspended by the magnetic force, as shown in the Figure. If the field lines crossing the loop make an angle %theta with the vertical, show that the strength of the magnetic force is:

F = mg over {2 %pi RI sin %theta}

Problem 3 (Halliday, Resnik)	Figure 2

Figure 2 shows four identical currents i and five Amperian paths encircling them. Rank the paths according to the value of f B, most positive first.